WAGT 220 DC RaSB

WELDING GEN-SET

ALTERNATOR			NSM

Type:					with brushes, for DC welding

Welding current:			40 ... 220 A

Strike voltage:			65-85 V

Duty cycle:				220A-35% / 170A-60%

Max. power:				6.5 kVA (3~) / 3.5 kVA (1~)

Cos Ø:				0,8 (3~) / 1 (1~)

ENGINE				RATO

Type:					OHV, 1 cylinder, 4 stroke, air cooled

Model:				R420

Displacement:			420 cm 3

Max. power:				15.0 HP

Piston stroke x diameter:		90mm X 66mm

Compression ratio:			8.5 : 1

Fuel:					unleaded gasoline

Starting system:			recoil

Consumption:			313 g/kWh

gEN-SET

Max. welding current:		200 A, at 35%

Max. electrode diameter:		4.0 mm

Voltage:				400 V (3~) / 230 V (1~)

Frequency:				50 Hz

Max. output:			6.5 kVA (3~) / 3.5 kVA (1~)

Fuel tank capacity:			6.5 l

Speed:				3.000 rpm

Dimensions:				820x548x568 mm(L x l x h)

Weight:				89 kg

Standard equipment:		1 single phase 16 A schu-ko socket

1 three phase 16 A CEE type socket

outlets for welding current

step-regulation knob for the welding current

thermal contact breaker

oil level sensor

hour counter

Optionals:				wheels and handle system

Welding cable set